## Slide 1
Submarine Simulation Design

## Slide 2
The goal of this exercise is to learn to implement a physics model in a Trick simulation in a clear and organized way.
“The computing scientist’s main challenge is not to get confused by the complexities of his own making.”
― Edsger W. Dijkstra

## Slide 3
In this simulation, we’ll control the position of the submarine by pumping air into or out of a ballast tank, which in turn displaces water.
Project: Submarine Simulation
Using Newton’s Second Law, and only the forces of gravity, buoyancy and hydrodynamic drag, described in the following pages, complete a Trick based simulation which continuously computes the position and velocity of a submarine.
In this simulation, we’ll assume that there is no loss of energy due to cooling of ballast air.
The submarine will only move in one-dimension, that is up or down.
Simplifications
Control

## Slide 4
Acceleration is a rate of velocity change .
Velocity is a rate of position change.
Current is a rate of change of charge.
General Strategy for Developing a Dynamic Simulation
“Dynamic” means “characterized by change”.
In a dynamic simulation things like position, and velocity, continuously change over time. Lots of other things might change as well depending on what you are simulating. The amount that something changes per unit of time is its rate of change, or time derivative.
If we know the rate of change of something, then we can add up all the little
changes over time to keep track of its value. This “adding up the little pieces” is called “numerical integration”.
This is the basic strategy for designing Trick dynamic simulations. We calculate rates, and then we numerically integrate them.
For example:

## Slide 5
To determine the motion of an object we generally start with Newton’s Second Law:
Solving for acceleration, we get :
That is, force equals mass times acceleration.
So, if we have a force acting on a mass, we can determine its acceleration. Then, we can then numerically integrate that acceleration to get velocity and then integrate the velocity to get position.
F = ma
a = F/m
This allows us to determine the rates that effect motion, that is: acceleration and velocity.
General Strategy for Motion
This is the form of Newton’s Law that we generally use.
In our simulation our rates will be acceleration, velocity, and power. For each time step (𝜹t) of our simulation, we’ll integrate our rates over the time period t  t + 𝜹t to get the next velocity, position, and energy state. A Trick integration job will calculate this for us.

## Slide 6
1.30 m
1.25 m
1.10 m
1.00 m
Ballast Tank Volume = 1.0 m3
3.0 m
Coefficient of Drag (Cd) = 0.5
Mass of Empty Submarine
10000.0 kilograms
Specifications of Our Submarine
You’re right! It’s an ugly submarine,
but it simplifies the simulation modeling.

## Slide 7
Ballast Air
(compressed air that we pumped in)
Ballast Water
(water that is in the ballast tank)
NOTE that the ballast air volume
plus, the ballast water volume
is the ballast tank volume.
More Terms

## Slide 8
A Bit About the Ideal Gas Law
PV = nRT = Energy in the system (E)
If we compress air in a container, its volume will go down, and its pressure will go up.
If we then decompress the air, its volume will go up and, its pressure will go down.
If the system doesn’t lose heat, which we will assume for simplicity, the energy (E) will remain the same. So, P = E/V and V = E/P.
If we have a fixed amount of air in the ballast tank, its volume will decrease as pressure increases. What doesn’t change is the product of P and V, that is the energy (E). So, we will control the buoyancy of the submarine by pumping energy into the system, which we’ll call ballast energy. Then we can calculate the volume from: V = E/P.

## Slide 9
To calculate acceleration, we’ll use Newton’s Second Law as usual. The force is the total force acting on the aircraft.
Acceleration
(1)
The total force on our aircraft is the sum of:
the thrust force produced by the aircraft’s engine and
the drag force produced by the aircraft pushing through the atmosphere.
If we affix a “Body” coordinate system to the submarine as shown, then the gravity force will act in the -y direction, and the buoyancy force in the +y direction. The drag force points the opposite direction of motion.
Notice that force is a vector. That is, it has a magnitude, and a direction.
(2)
FGravity
FBuoyancy

## Slide 10
Gravity Force
Fgravity = mtotal· g
What determines the mass of the submarine?
Applying the acceleration of gravity to Newton’s 2nd Law:
At sea-level, g is around 9.81 m/s2. Since our submarine will at most descend a few miles, we’ll
treat g as a constant.
(3)

## Slide 11
Submarine Mass
hull
payload (passengers, etc.)
--------------
mfixed
mtotal = mfixed + mhard_ballast + mballast_water
What’s the mass of the ballast water in the submarine?
mhard_ballast
10000.0 kg
1500.0 kg
--------------
11500.0 kg
0.0 kg
(4)

## Slide 12
Ballast Water Mass
Vballast_water = Vballast_tank – Vballast_air
mballast_water = Vballast_water ⨯ 𝝆water
(5)
(6)
ballast_air_ratio = Vballast_air / Vballast_tank
(6.a)
We also need to calculate the ratio of the ballast air to ballast tank
volume for our GUI, to draw the water and air in the ballast tank.
The mass of the water in the ballast tank is the volume of
the water in the ballast tank times the density of water.
The volume of the water in the ballast tank is the volume
of the ballast tank minus the volume filled with air.

## Slide 13
Ballast Air Volume
Vballast_air = Eballast / Pwater
Note that we must limit the volume of the ballast air to that of the ballast tank. That is Vballast_air must be limited to less than or equal to Vballast_tank
Also, when we limit Vballast_air we must recalculate Eballast
What’s the water pressure (Pwater)
at our submarine’s depth?
(7)

## Slide 14
Water Pressure
Pwater = 𝝆water ⨯ g ⨯ depth + Patmosphere
• 𝝆water is the density of water.
• g is the acceleration of gravity.
• depth is our submarine’s depth below the surface. Note that this is the negative of our submarines y-position.
• Patmosphere is the atmospheric pressure at the surface of the water.
(8)

## Slide 15
Drag Force
As the submarine moves upward, or downward, it will be subject to an drag force. Drag is a function of the submarine’s shape [ presented by the coefficient of drag (Cd)], the density of the water (𝝆), and the cross-sectional area (A) perpendicular to the velocity (v). The drag force points in the opposite direction as the velocity.
Fdrag = - ½ 𝝆 v|v|Cd A
For our submarine, we’ll assume Cd = 0.5, the coefficient of drag for a sphere.
A = outer_hull_outer_radius ⨯ 2 ⨯ hull_length
𝝆 (Density of Salt Water) = 1023.6 kg/m3
We’ll calculate the cross-sectional area from the outer radius of the outer hull of our submarine (Eq#).
(9)
(10)

## Slide 16
Fbouyancy = mdisplaced_water· g
Buoyancy is a force on an object, that opposes gravity, by a fluid within which it’s immersed. This force is equal to the mass of the displaced fluid times the acceleration of gravity.
mdisplaced_water = ( Vhull_disp + Vballast_air ) · 𝝆water
• Vhull_disp is the volume of water displaced by the hull.
• Vballast_air is the volume of air in the ballast tank. Note that this air displaces water from the ballast tank. This was calculated in equation #7.
• 𝝆water is the density of water.
Force of Buoyancy
(11)

## Slide 17
Vhull = 𝝅 ⨯ (inner_hull_outer_radius)2 ⨯ hull_length
Vhull / (1 + e( -5.5 depth))
if hull is not submerged.
0
Vhull
if hull is partially submerged,
We can estimate the displacement.
if hull is fully submerged
Vhull_disp =
(12)
(13)
Hull Displacement Volume

## Slide 18
Side-Note About the Partially Submerged Hull Estimate
In the special case where the submarine is only partially submerged, we estimate the volume of water displaced by
the hull using a sigmoid (S-shaped) function.

## Slide 19
Organizing Things
We now have the equations needed to calculate our acceleration, forces, masses, volumes, densities, so forth. On the next few pages, we’ll look at our variables in terms of computational dependencies. This exercise can give us some valuable insight as to how we organize our simulation.

## Slide 20
Fbuoy
mtotal_displacement
g
Eballast
Pwater
Vhull_disp
posy
g
𝞺water
Vballast_air
acc
Fg
Fdrag
Cd
vel
A
mtotal
g
mfixed
mballastWater
VballastWater
VballastTank
𝞺water
mhardBallast
inner_hull_outer_radius
Ftotal
Eq3
Eq4
Eq5
Eq6
Eq7
Eq8
Eq9
Eq11
Vhull
hull_length
Eq13
Eq12
Eq1
Eq2
velnext
vel
pos
posnext
Computational Dependencies
Integration
Integration
Eballast_next
pump_power
Eballast
Integration
Numerical Integration
From the GUI, that is, the
variable server client.
GUI
hull_length
outer_hull_outer_radius
Eq10

## Slide 21
class Submarine {
public:
// Parameters
double outer_hull_outer_radius;
double inner_hull_outer_radius;
double hull_length;
double ballast_tank_volume;
double hard_ballast_mass;
double hull_mass;
double payload_mass;
double Cd;
// State Variables (Uncalculated Variables)
double pos[2];
double vel[2];
double ballast_energy; // joules
double pump_power; // watts
// Calculated Variables
double acc[2];
// Control Variable
double ballast_air_ratio; // To the GUI.
double water_pressure_pascals;
double water_pressure_PSI; // To the GUI.
int pump_power_command; // From the GUI.
What are the members of the struct or class that describes our submarine?
In the dependencies tree, the variables that don’t have dependencies (in the yellow boxes), completely define the parameters of our submarine. The variables derived by numerical integration (in the green boxes) define the dynamic state of the submarine. Let’s start with these.
Whereas pos and vel are 2-D arrays we’re only going to update the vertical element (y) for now.
Finally, we need some control variables for communicating with our variable server client.
Submarine Simulation State

## Slide 22
outer_hull_outer_radius = 1.30 meters
outer_hull_inner_radius = 1.25 meters
inner_hull_outer_radius = 1.10 meters
inner_hull_inner_radius = 1.00 meters
hull_length = 3.0 meters
Density of Salt Water (𝞺) = 1023.6 kg/m3
Acceleration of gravity (g) = 9.80665 m/s2
Atmospheric pressure = (Patmosphere) = 101353.0 pascals = 14.7 lbs/inch2
Position of the submarine : (0, 0) m.
Velocity of the submarine : (0, 0) m/s.
Fixed mass components of the submarine
The coefficient of drag (Cd) : 0.5.
ballast_tank_volume = 1.0 cubic meters
Dimensions of the submarine
  hull_mass = 10000.0 kilograms
  hard_ballast_mass= 0.0 kilograms
  payload_mass = 1500.0 kilograms
Default Values
Notes: hull_length = 3.0;